## Slide 1
Multi-Criteria Sustainability Optimisation
of Floor Slabs
Beyond Structural Performance in Early-Stage Design
Jonathan Bieg
Master Thesis - Final Presentation
29 June 2026

## Slide 2
Table of content
Institute of Structural Engineering
Multi-criteria sustainability optimisation of floor slabs
2
Introduction
Objective and contribution
Methodology
Results and discussion
Conclusion
Outlook

## Slide 3
Introduction - Challenge for the construction industry
Institute of Structural Engineering
Introduction
3
Why floor systems matter
- Buildings are a major source of material demand and emissions.
- Floor slabs repeat over many storeys and strongly influence mass, height and construction process.
- Early design decisions lock in much of the later sustainability performance.
Goal
Make floor-system selection comparable beyond structural performance alone.
Sustainability is assessed through GWP, cost, construction time, height and mass while all required structural and functional criteria are fulfilled.

## Slide 4
Objective and research questions
Institute of Structural Engineering
Objective
4
Objective
Assess the sustainability impact of choosing a floor system for residential and office buildings in early-stage design.
1
Which assessment criteria are relevant for early-stage floor-system comparison?
2
Which systems perform favourably when structural and functional requirements are respected?
3
How do Global Warming Potential and construction cost align or conflict?

## Slide 5
Methodology - Slab configurator workflow
Institute of Structural Engineering
Methodology
5
Contribution
- Existing Python framework extended for consistent comparison.
- New floor systems: timber-concrete composite and post-tensioned concrete.
- Automated acoustic floor build-up handling added.
- Pairwise comparison ranks systems while accounting for data variation.

## Slide 6
Methodology - Compared systems and requirements
Institute of Structural Engineering
Methodology
6
Residential
Concrete
Timber
Timber-concrete composite
Office
Concrete systems
Post-tensioned layouts
Ribbed concrete
Requirements
ULS
Deflection
Vibration
Fire
Acoustics
Comparison is performed for complete floor systems, not only the bare structural cross-section.

## Slide 7
Methodology - New model components
Institute of Structural Engineering
Methodology
7
TCC
Post-tensioning
Floor build-up
- Semi-rigid composite action
- Flat and ribbed alternatives
- Distributed and banded tendons
- Secondary moments and punching
- Acoustic requirements
- Mass, height, cost and GWP added

## Slide 8
Verification and comparison setup
Institute of Structural Engineering
Methodology
8
Validation before comparison
- Timber-concrete composite stiffness checked against reference calculations.
- Post-tensioned concrete class validated for bending resistance and deflection.
- Acoustic build-up generator checked against Lignum reference constructions.
Final comparison
- Optimise each system with respect to GWP while fulfilling all requirements.
- Evaluate GWP, cost, time, height and mass over relevant span ranges.
- Use envelopes and pairwise scores to handle variation in product data.
Core principle: compare feasible alternatives, not idealised material stereotypes.

## Slide 9
Results - Residential floor systems
Institute of Structural Engineering
Results
9
- Timber performs favourably at short spans but becomes sensitive to vibration and height.
- Rectangular concrete is balanced at intermediate spans.
- TCC and post-tensioned concrete become competitive at longer spans.

## Slide 10
Results - Residential application ranges
Institute of Structural Engineering
Results
10
Interpretation
- No single system dominates all spans and criteria.
- Use rectangular timber only where short spans keep height and cost controlled.
- Use concrete or post-tensioned concrete as span increases.
- Flat TCC is a robust compromise across residential spans.

## Slide 11
Results - Office floor systems
Institute of Structural Engineering
Results
11
- Post-tensioning improves deflection, punching and material demand at larger spans.
- Banded tendons perform best in the current model because tendons align with support strips.
- Ribbed concrete has low GWP and mass, but requires more construction height.

## Slide 12
Results - Office application ranges
Institute of Structural Engineering
Results
12
Recommendation
- Rectangular reinforced concrete is not recommended for the investigated span range.
- Banded post-tensioned concrete provides the best overall balance.
- Ribbed concrete is attractive from approximately 10 m, unless height governs.

## Slide 13
Discussion - GWP and construction cost
Institute of Structural Engineering
Discussion
13
Residential
Weak correlation: r = 0.17
- Low-GWP timber is modelled as higher cost.
- Concrete tends to be cheaper but has higher GWP.
- TCC systems become compromise solutions.
Office
Strong correlation: r = 0.96
- All systems are concrete-based.
- Material efficiency reduces both GWP and cost.
- Height remains the key counter-criterion.

## Slide 14
Discussion - Relevant sustainability criteria
Institute of Structural Engineering
Discussion
14
Primary
GWP
Construction cost
Boundary / project-specific
Height
Construction time
Context-dependent
Mass
Material variation
The complete floor system matters: acoustic build-ups can change rankings, especially for timber and TCC residential systems.

## Slide 15
Limitations
Institute of Structural Engineering
Conclusion
15
- Results are early-stage comparison results, not final project-specific design recommendations.
- Application ranges depend on loads, span ranges, acoustic requirements, height constraints and construction processes.
- Cost and time models simplify fabrication, logistics and connection effort.
- Ribbed timber hollow-core results are sensitive to fire verification and insulation assumptions.
Main value of the configurator: a consistent, transparent decision basis for comparing feasible floor systems early.

## Slide 16
Conclusion and outlook
Institute of Structural Engineering
Conclusion
16
Conclusion
- GWP and cost should be treated as primary criteria.
- Residential design contains a real ecological-economic trade-off.
- Office long-span design benefits from structural efficiency: post-tensioned and ribbed systems align cost and GWP.
- Floor height can decide whether a low-GWP system is actually usable.
Outlook
- Improve fire verification and insulation data for timber hollow-core systems.
- Separate material, fabrication and installation in cost and time databases.
- Test sensitivity to changed loads, acoustic requirements and height limits.
- Develop a web interface for criterion weighting in practice.
Thank you